## Slide 1: NoRD: Node-Router Decoupling for Effective Power-gating of On-Chip Routers
Lizhong Chen - Timothy M. Pinkston - 2012
Ming Hsieh Department of Electrical Engineering
University of Southern California Los Angeles, CA

## Slide 2: Outline
Context and Motivation
Proposed design
Evaluation
Conclusion

## Slide 3: Context
Power off the router
  Buffer empty and notifying all of neighbors by PG signal
Awake the router when
  Any neighbors assert WU signal
  Neighbors wait for PG signal to clear
Effectiveness subject to
  Wakeup latency (~12 cycles for router)
  Breakeven-time (BET)
    The minimum number of consecutive gated-off idle cycles to offset power-gating energy overhead (~10 cycles for router)
WU
PG
Router
A
Router
B
Router
D
WU
PG
Router
C
WU
PG
Router
E
WU
PG

## Slide 4: Motivation
BET limitation is intensified
  61% of the total number of idle periods has length less than BET!
  Cumulative wakeup latency in multi-hop NoCs
  Disconnection problem
2
0
1
3
4
5
6
7
8
9
10
11
12
13
14
15
S
D
The reason: node-router dependence
NoRD (Node-Router Decoupling) - a novel approach that provides separate power-gating bypass to decouple the node’s ability for transferring packets from the status of the router.
Node 2
Notes:   Intermittent packet arrivals => fragmented idle intervals
any packet (sent, received or forwarded) must wake up the router before being transfer red, thus breaking the potentially long idle period into fragmented intervals.

## Slide 5: Outline
Context and Motivation
Proposed design
Evaluation
Conclusion

## Slide 6: NoRD Bypass Paths
Add two bypass paths to each router
  One bypass from Bypass Inport to the NI ejection
  One bypass from the NI injection to Bypass Outport
Chip-level Bypass Ring
Bypass datapath in router

## Slide 7: NoRD Bypass Paths
State-transitions
  On -> off, when the datapath of router is empty
  Off -> on, when a wakeup metric exceeds a threshold
①
③
Network Interface
Low implementation cost of decoupling bypass paths and forwarding logic: 3.1% of router area

## Slide 8: NoRD routing
Based on Duato’s Protocol for fully adaptive routing
  Minimal path along gated-on routers & gated-off routers
2
0
1
3
4
5
6
7
8
9
10
11
12
13
14
15
S
D
D

## Slide 9: NoRD routing
Based on Duato’s Protocol for fully adaptive routing
  Minimal path along gated-on routers & gated-off routers
  Limited misroutes possible only if all routers off along min path
  Bypass Ring serves as “escape path”
2
0
1
3
4
5
6
7
8
9
10
11
12
13
14
15
S
D
D

## Slide 10: Increasing NoRD Efficiency
Differentiate routers
  Routers have different impact on performance based on their locations in the NoC
Performance-centric class vs. Power-centric class
  Wake up early a few performance-critical
  routers to add “shortcuts” in routing
  Wake up late the rest (majority) of the
  routers to save more static power
  Use an off-line program to classify
  the routers
2
0
1
3
4
5
6
7
8
9
10
11
12
13
14
15

## Slide 11: Router states transition
Power-off router B
  IC and WU are clear
  Routers C, D, E tag output
  Router A sets the credit of each VC in that output port to 1 as router B now has only one output buffer available
Power-on router B
  WU signal active: according to the wake-up threshold (when the load is high)
  Routers C, D, E reset
Wake-up threshold
  VC request rate

## Slide 12: Outline
Context and Motivation
Proposed design
Evaluation
  No_PG - No power-gating
  Conv_PG - Conventional power-gating
  Conv_PG_OPT - Early wakeup optimization power-gating
  NoRD - Node-router decoupling
Conclusion

## Slide 13: Environment
Core 90 mn

## Slide 14: Evaluation
Static energy saved
  Conv_PG: 51.2%, Conv_PG_OPT : 47.0%, NoRD: 62.9%
NoRD reduces power-gating overhead and number of router wakeups by over 80%
Overall NoC energy saved
  Conv_PG: 9.4%, Conv_PG_OPT: 9.1%, NoRD: 20.6%
  Static energy savings exceed dynamic energy losses
Average packet latency penalty
  Conv_PG: 63.8%, Conv_PG_OPT: 41.5%, NoRD: 15.2%
Execution time penalty
  Conv_PG: 11.7%, Conv_PG_OPT: 8.1%, NoRD: 3.9%

## Slide 15: Conclusion: NoRD
Optimization
  Significantly reduces the number of power state transitions
  Increases the length of idle periods
  Completely hides the wakeup latency from the critical path
  Eliminates network disconnection problems
Limitation
  Maybe increases the packet latency by detouring it to a neighbour router
  NoRD is not scalable for large NoC
Reduce the router static energy by 29.9% and improve the average packet latency by 26.3%, with only 3% additional area overhead.

## Slide 16: Thank you for your attention