## Slide 1: Run-Time Power Gating of On-Chip Routers Using Look-Ahead Routing
Hiroki Matsutani - Michihiro Koibuchi
Daihan Wang - Hideharu Amano
(Keio Univ, Japan)

## Slide 2: Outline
On-Chip Router
  Architecture
  Power consumption
Runtime power gating of routers
  Overheads
  Look-Ahead sleep control
Evaluations
  Performance penalty
  Compensated sleep cycles
  Leakage reduction

## Slide 3: On-Chip Router: Architecture
5-input 5-output router (data width is 64-bit)
5x5 XBAR
ARBITER
FIFO
FIFO
FIFO
FIFO
FIFO
X+
X-
Y+
Y-
CORE
X+
X-
Y+
Y-
CORE
Two virtual channels
(64-bit x 4 x 2)
HW amount is 34 kilo gates and 64% of area is used for FIFO

## Slide 4: On-Chip Router: Pipeline
A header flit goes through a router in 3 cycles
  RC (Routing Computation)
  SA (Switch Allocation)
  ST (Switch Traversal)
E.g., Packet transfer from router A to C

## Slide 5: On-Chip Router: Power consumption
Place-and-routed with 90nm CMOS
Post layout simulation at 200MHz
Power consumption of a router when n ports are used [mW]
Notes: A router consumes more power as the router processes more packets

## Slide 6: Outline
Network-on-Chip (NoC)
On-Chip Router
  Architecture
  Power consumption
Runtime power gating of routers
  Basic sleep control
  Look-Ahead sleep control
Evaluations
  Performance penalty
  Compensated sleep cycles
  Leakage reduction

## Slide 7: Basic Sleep Control
Basic Routing:
  Router i calculates the output port of Router i
Basic Sleep Control
=> performance penalty due to the wake-up delay
depends on how early the new requests can be detected

## Slide 8: Look-Ahead Sleep Control
Look-ahead Routing:
  - Router i calculates the output port of Router i+1
  => To mitigate the wakeup delay and short-term sleeps
R0
R1
R2
R3
R4
R5
R6
R7
R8
Five-cycle margin until packet arrival
R2 detects a packet arrival when the packet arrives at R4
Look-Ahead:
RC
SA
ST
ST
ST
ST
RC
SA
ST
ST
Router 4
Router 5
Router 2
RC
Packet will arrive after two hops
Look-ahead can eliminate a wakeup delay of less than 5-cycle

## Slide 9: Look-Ahead Sleep Control
Call South channel of router 1 is “target”. The target channel monitor request signal from input channel in router 3, 5, 7 to make decision.
The colored input channel assert their request signal for the target channel when packet destined for router 1.
Critical path twice long, so can using 2 clock cycle to transfer for target channel

## Slide 10: Outline
On-Chip Router
  Architecture
  Power consumption
Runtime power gating of routers
  Overheads
  Look-Ahead sleep control
Evaluations
  Performance penalty
  Leakage reduction

## Slide 11: Evaluations: Simulation
Environment
  Synopsys Power Compiler 90nm

## Slide 12: Evaluations: Sleep control methods
Evaluation items
  Network throughput
  Leakage reduction
Parameters
Ideal method
  Ideal case
  No wakeup delay
Look-ahead method
  Detects packet arrival 5-cycles ahead
Naïve method
  No look-ahead
Topology | 2-D Mesh (4x4)
Routing | DOR (XY routing)
Packet size | 5-flit (1-flit header)
Buffer size | 4-flit (WH switching)
# of VCs | 2 VCs
Latency | 3-cycle per 1-hop

## Slide 13: Evaluations: Performance of “lookahead”
Throughput on various wakeup delays (e.g., 0,1,2,3 cycles)
  Naive: Performance is degraded as Twakeup increases
  Ideal: Same
  Look-ahead: Same if Twakeup is less than 5

## Slide 14: Evaluations: Leakage power reduction
Leakage power at each channel Tbreakeven = 6
  No power gating consumes 95 [uW]
  Leakage reduction of PG with 3 sleep control methods
Uniform traffic (16-core)
- Leak increases as traffic increases
=> Ideal <Look-ahead < Naive
Leakage reduction

## Slide 15: Summary: Look-ahead sleep control
Runtime power gating of router channels
  Wakeup delay introduces pipeline stalls of routers
  Short-term sleeps overwhelm the leakage reduction
Look-ahead sleep control
  An extension of “look-ahead routing”
  Detects the arrival of packets five cycles ahead
Evaluation results
  Look-ahead conceals the wakeup delay of less than 5
  Look-ahead reduces more leakage compared with naive

## Slide 16: Thank you for your attention

## Slide 17: Backup slides

## Slide 18: Look-ahead method: HW resources
Routing computation of next router
  Just changing the routing function
  Area overhead is very small
Wakeup signals are needed
  Sender asserts “wakeup” signal
  to receiver
  Wakeup signals becomes long
  Negative impact of
  multi-cycle or repeater buffers
NRC
SA
ST
ST
ST
NRC
SA
ST
ST
ST
NRC
SA
ST
ST
ST
HEAD
DATA 1
DATA 2
NRC stage: Next Routing Computation
0
1
2
3
4
5
6
7
8
Wakeup signals to router 1

## Slide 19: Look-ahead method: the 1st hop?
Look-ahead for Router 3, Router 4, Router 5, …
Look-ahead for Router 1 and Router 2
Network interface (NI) performs look-ahead
  Packet construction takes several clock cycles
  NI of source node can perform “look-ahead”
Router (1)
Src
Dst
Look-ahead!!
Router (2)
Router (3)
Router (4)
Look-ahead!!
Router (1)
Src
Dst
Router (2)
Router (3)
Router (4)
Look-ahead!!