## Slide 1: Traffic-Aware Power-Gating Scheme for Network-On-Chip Routers
Nasim Nasirian∗, Reza Soosahabi†, Magdy Bayoumi∗
2016

## Slide 2: OUTLINE
Context and Motivation
Proposed Design
Experimental results
Conclusion

## Slide 3: Context and motivation
Network-on-chip
Power gating
  Power reduction
  Delay, power overhead
Traffic-aware
  - Traffic inter-arrival times estimation
  - Decision
Notes: Traffic-aware la 1 thiet ke dieu khien tin hieu power-gating dua tren su uoc luong khoang thoi gian giua cac lan den
Hinh tren la bieu do cac khoang chinh trong 1 chu ki power-gating

## Slide 4: Propose design
Router Architecture
State Diagram of Buffers
Notes: - Cap phat kinh ao
Bo phan xu
Th1: T breakeven
Th2: T weakup delay

## Slide 5: Inter-arrivel times estimation
  The inter-arrivel time denoted by random variable X follows the Gamma distribution
  Gamma function:
  Gamma PDF:

## Slide 6: Result
Training data (NOXIM):
  α = 1.148, β = 7.73529 in 4 × 4 network
  α = 0.87, β = 7.236 in 8 × 8 network
Hardware implementation
  (Synopsys 45nm technology in 500 MHz)
  Improving 25% static power consumption
  Reducing 35% the average packet latency
  Decreasing 41% overhead compare with look-ahead routing approach (Matsutani-2008)
Area increase 15%

## Slide 7: Thank you for your attention !